## Slide 1: OMG Systems Modeling Language (OMG SysML™) Tutorial
September, 2009
Sanford Friedenthal Alan Moore
Rick Steiner
(emails included in references at end)
Copyright © 2006-2009 by Object Management Group.
Published and used by INCOSE and affiliated societies with permission.

## Slide 2: OMG SysML™ Specification
2
Specification status
  Adopted by OMG in May ’06
  Available Specification v1.0 in Sept ’07
  Available Specification v1.1 in Nov ‘08
  Revision task force for v1.2 in process
Multiple vendor implementations available
This tutorial is based on the OMG SysML available specification (formal/2007-09-01)
This tutorial, the specifications, papers, and vendor info can be found on the OMG SysML Website at http://www.omgsysml.org/
Refer to “A Practical Guide to SysML” by Friedenthal, Moore, and Steiner for language details and reference

## Slide 3: Objectives & Intended Audience
2
At the end of this tutorial, you should have an awareness of:
Motivation of model-based systems engineering approach
SysML diagrams and language concepts
How to apply SysML as part of a model based SE process
Basic considerations for transitioning to SysML
This course is not intended to make you a systems modeler!
You must use the language.
Intended Audience:
•
Practicing Systems Engineers interested in system modeling
Software Engineers who want to better understand how to integrate software and system models
Familiarity with UML is not required, but it helps

## Slide 4: Topics
2
Motivation & Background
Diagram Overview and Language Concepts
SysML Modeling as Part of SE Process
  Structured Analysis – Distiller Example
  OOSEM – Enhanced Security System Example
SysML in a Standards Framework
Transitioning to SysML
Summary
Class Exercise

## Slide 5: Motivation & Background

## Slide 6: SE Practices for Describing Systems
Specifications
Interface requirements
System design
Analysis & Trade-off
Test plans
Moving from Document centric to Model centric
Past
Future

## Slide 7: System Modeling
Start
Shift
Accelerate
Brake
Engine |  | Transmission |  | Transaxle
Control Input
Power Equations
Vehicle Dynamics
Mass
Pr
operties
odel
al
M Structur
M
odel
ty
Safe M
odel
Cost Model
Requirements
Integrated System Model Must Address Multiple Aspects of a System

## Slide 8: Model Based Systems Engineering Benefits
Shared understanding of system requirements and design
  Validation of requirements
  Common basis for analysis and design
  Facilitates identification of risks
Assists in managing complex system development
  Separation of concerns via multiple views of integrated model
  Supports traceability through hierarchical system models
  Facilitates impact analysis of requirements and design changes
  Supports incremental development & evolutionary acquisition
Improved design quality
  Reduced errors and ambiguity
  More complete representation
Supports early and on-going verification & validation to reduce risk
Provides value through life cycle (e.g., training)
Enhances knowledge capture

## Slide 9: System-of-Systems
Interactions
Boundaries
Modeling Needed to Manage System Complexity

## Slide 10: Modeling at Multiple Levels of the System
TITLE>System Design<TITLE>
META http-equiv="REFRESH"
!--CSSDATA:966533483-->
SCRIPT src="/virtual/2000/code
LINK rel="stylesheet" href="/
<
<
<
<
<
<
SCRIPT language="javascript"
Data Processing Terminal Hardware
TCIM
Voice Comm Hardware includes MSE
Voice Comm Hardware includes MSE
Power Generation and Distribution
EPLRS or SINGARS
Terminal
EPLRS or SINGARS
Terminal
JTIDS
Terminal
PLGR (GPS)
PLGR (GPS)
Software
A2C2 Subsystem
ABMOC Subsystem
Operator Interface
Hardware
Data Processing Terminal Hardware
Software
Power Force Level
Control System
Power
Power
Power
Power
Power
Power TCIM
Voice & TADIL-B Data
Power Generation and Distribution
Power
Power
Power
Power Force Level
Control System
Operator Interface Hardware |  | 
 | Power | 
Power JTIDS
Terminal
Power Voice & TADIL-B Data
Tech Support System Entry
Primary Key
TSS_Entry_Number [PK1]
Non-Key Attributes
Windows_Version
TSS_Description
Primary Key
Serial_Number [
PK1] [FK]
Location Primary Key
Status [PK1] [FK]
Software Release Primary Key Version_Number [PK1]
Status [PK1]
consists of
Customer Software License
Primary Key Primary Key is subj
Customer_ID [PK1] owns Serial_Number [PK1]
Non-Key Attributes Non-Key Attributes
Customer_Name Technical_Contact Purchase_Contact
Customer_Address
ect to Client Call
creates
currently has
Status
is a Primary Key
CEC Inform ation Exchange Require m ents - Class ifie d SECRET when filled in
2 3 4 5 6 7 8 9 10 11
on Inform ation Characte rization Se nding Re ceiving Critical Form at Class Late ncy: SA/Eng Me ss age Rem ark s
Node Node Support Error Rate
A/Support Radar m e asurem e nts to REF: CEC A-spec
nts support data fus ion com posite Host CEP Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % Table 3-3 and track ing Hos t re qm ts
track ing
A/Support IFF m e as urem e nts to support
nts data fus ion and com pos ite Host CEP Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx %
1
Rationale/UJTL Num ber Event/Acti
OP 5.1.1 Com m Op Info Provide S
Engage m e
OP 5.1.1 Com m Op Info Provide S
Engage m e
OP 5.1.1 Com m Op Info Provide S
Engage m e
OP 5.1.1 Com m Op Info Provide S
Engage m e
OP 5.1.1 Com m Op Info Provide S
Engage m e
A/Support IFF inte rrogation re que sts to Res pond w he n
nts support data fus ion and Host CEP Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % requested com posite tracking
A/Support ID Change s to s upport data Host CEP Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % nts fusion and com posite track ing
A/Support Navigation data to support data Host CEP Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % REF:CEC SRS and nts fusion and com posite track ing Host Nav. spec
Provide SA/Support Engagem e nt Support Reque sts
OP 5.1.1 Com m Op Info Engage m e nts to support data fus ion and Host CEP Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % AEGIS only com posite tracking
Provide SA/Support Track num ber m anagem e nt to Changes se nt
OP 5.1.1 Com m Op Info Engage m e nts support data fus ion and Host-CEP CEP-Host Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % immediately com posite tracking
Provide SA/Support Com pos ite Track State Update REF: CEC IDDs for
OP 5.1.1 Com m Op Info Engage m e nts to support data fus ion and CEP Host Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % each host com posite tracking
Provide SA/Support Ass ociate d M e asurem e nt REF: CEC A-spec
OP 5.1.1 Com m Op Info Engage m e nts Re ports to support data fus ion CEP Host Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % Table 3-3. SPY and com posite track ing
only
track ing
Provide SA/Support IFF As signm e nts to support Whe n ass igned
OP 5.1.1 Com m Op Info Engage m e nts data fus ion and com pos ite CEP Host Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % or change d
Provide SA/Support ID recommendations to Whe n ass igned
OP 5.1.1 Com m Op Info Engage m e nts support data fus ion and CEP Host Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % or change d com posite tracking
Provide SA/Support Se ns or cue s to s upport data REF: CEC A-spec
OP 5.1.1 Com m Op Info Engage m e nts fusion and com posite track ing CEP Host Ye s Binary IAW IDD Se cret xx s ecs/xx se cs xx % Table 3-3. SPY
only
corr fail / is new BMDS Track
corr success / is corr BMDS Track
Receiving Network Track File
Data
On entry / receive file data Do / store track data
On exit / request matching data
Receiving BMDS Track File Data
On entry / receive file data Do / store track data
Idle
Session Activated
BMDS Track File Request Sent ( Request
) / Pull BMDS Track Files
Network Track File Received ( File Data ) [ number tracks
> 0 ] / Input Network Track
Correlation Complete ( C
Results ) [ set not null ] / Se
Correlating Tracks
On entry / match state vector Do / corr state vectors
Do / corr LPE Do / corr PIP Do / corr RCS Do / corr CID
orrelation
nd Result
s
On exit / corr BMDS Track #
s
BMDS Track File Data Received ( File Data ) / Correlate Tracks
/ initialize
Verify CID, Correlation, and Assoicated Track Data
Monitor Correlation Process
Create New BMDS Track
nd Track
e Data
Update Track
HIC
ack File
ule
k s
Network Track MSG
Track MSG Data Send BMDS Track Data to
JDN
Prepared Track MSG
BMDS Track Data
BMDS Track Display
Correlation no Possible
yes File Data
Correlation Results
BMDS Track Data Correlate Tracks BMDS Track Data
TrTr
Track F
Track Data Se
Fil
ile Request
NetworkNetwork InterfaceInterface TrackTrack ManagementManagement ModuleModule CorrelationCorrelation Mod
ModuleModule
Attempt to Request
Track Data Correlate with Track Data Possible BMDS Track BMDS Trac
File Matche
ng
ng
TCIM
Voice Comm Hardware includes MSE
Hardware includes MSE
ace
ace
Force Level Control System
Power Generation and Distribution
EPLRS or SINGARS
Terminal
EPLRS or SINGARS
Terminal
JTIDS
Terminal
PLGR (GPS)
Software
ABMOC Subsystem
Power
Power
Power
Power
Power
A2C2 Subsystem Power
Power Generation and Distribution
Power TCIM
Voice & TADIL-B Data
Power
Power Voice Comm
Power
Power
Force Level Control System
Operator Interf
Hardware
Power
Data Processi Terminal Hardware
Software
PLGR (GPS)
Operator Interf Hardware
Data Processi Terminal Hardware
Power JTIDS
Terminal
Power Voice & TADIL-B Data
FAAD C3I
AMDPCS
Patriot ICC
MCE (CRC)
AWACS
MCE (CRC)
MCE (CRC)
LINK 16
LINK 16
LINK 16
LINK 16
<<entity>>
Network Track
receive () store () update () send ()
<<interface>>
Network Interface Module
buffer capacity
/msg data
receive msg () parse msg () route msg data () build msg () send msg ()
Correlation Module
algorithm
/tracks to be correlated correlation data decorrelation data
correlate tracks () decorrelate tracks () retrieve track data () send track data ()
Track Mangement Module
/current tracks
/associated track data
/CID data
assign CID () recommend CID () retrieve track file data () display track file data ()
<<entity>> Track File
Track Number CID
/State Vector
/Date-Time
send track data ()
<<entity>>
BMDS Track
create ()
update ()
destroy ()
retrieve ()
HIC
JDN
manages
0..*
1..*
1..*
correlates
0..*
1
communicates with
1
interface for
1 1
uses 1..*
1..*
received from
1
0..*
owning element <<derived>> /associated data
Received Date-Time traces to /history local track number
Track File
11
13
Track File Data
12
Files
Track Mangement S/W Module
Network Interface S/W
Correlation S/W
Module
Correlate Track Correlated Track
Network Plan
CID Criteria
Network Network Track Data Receive Network Track Data
JDN
HIC
Manage BMDS BMDS Track
AMDPCS
FAAD C3I
ACDS (CVN)
DDG-51 AEGIS Destroyer
F-15C
AWACS
F/A-18
MCE
TAOM
RIVET JOINT
CG
Patriot ICC
E-2C
SIAP
Operational Models
System Models
Component Models

## Slide 11: Stakeholders Involved in System Acquisition
Testers
Developers/ Integrators
Vendors
Regulators
Customers
Project Managers
Modeling Needed to Improve Communications

## Slide 12: What is SysML?
A graphical modelling language in response to the UML for Systems Engineering RFP developed by the OMG, INCOSE, and AP233
– a UML Profile that represents a subset of UML 2 with extensions
Supports the specification, analysis, design, verification, and validation of systems that include hardware, software, data, personnel, procedures, and facilities
Supports model and data interchange via XML Metadata Interchange (XMI®) and the evolving AP233 standard (in-process)
SysML is Critical Enabler for Model Driven SE

## Slide 13: What is SysML (cont.)
Is a visual modeling language that provides
  Semantics = meaning
  Notation = representation of meaning
Is not a methodology or a tool
  SysML is methodology and tool independent

## Slide 14: Diagram Overview & Language Concepts

## Slide 15: Relationship Between SysML and UML
4/15/2008
Copyright © 2006-2008 by Object Management Group.
15
UML
reused by SysML (UML4SysML)
UML
not required by SysML (UML - UML4SysML)
SysML extensions to UML (SysML Profile)
UML 2
SysML
SysML Extensions
-Blocks
-Item flows
-Value properties
-Allocations
-Requirements
-Parametrics
-Continuous flows
-…

## Slide 16: SysML Diagram Taxonomy
4/15/2008
Copyright © 2006-2008 by Object Management Group.
16
SysML Diagram
Use Case Diagram
Activity Diagram
Sequence Diagram
State Machine Diagram
Parametric Diagram
Behavior Diagram |  |  | Requirement Diagram |  |  | Structure Diagram | 
Modified from UML 2
New diagram type
Block Definition Diagram |  |  | Internal Block Diagram |  |  | Package Diagram | 
Same as UML 2

## Slide 17: 4 Pillars of SysML – ABS Example
4/15/2008 Copyright © 2006-2008 by Object Management Group.
17
definition
use
1. Structure
3. Requirements
4. Parametrics
sd ABS_ActivationSequence [Sequence Diagram]
d1:Traction Det
m1:Brake
ector Modulator
detTrkLos() sendSignal()
modBrkFrc(traction_signal:boolean)
modBrkFrc()
sendAck()
2. Behavior
interaction
state machine
activity/ function

## Slide 18: SysML Diagram Frames
Each SysML diagram represents a model element
Each SysML Diagram must have a Diagram Frame
Diagram context is indicated in the header:
  Diagram kind (act, bdd, ibd, sd, etc.)
  Model element type (package, block, activity, etc.)
  Model element name
  User defined diagram name or view name
A separate diagram description block is used to indicate if the
diagram is complete, or has elements elided
«diagram usage»
diagramKind [modelElementType] modelElementName [diagramName]
Header
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Contents
Diagram Description
Version: Description: Completion status: Reference:
(User-defined fields)

## Slide 19: Structural Diagrams
SysML Diagram
Use Case Diagram
Activity Diagram
Sequence Diagram
State Machine Diagram
Parametric Diagram
Behavior Diagram |  |  | Requirement Diagram |  |  | Structure Diagram | 
Block Definition Diagram |  |  | Internal Block Diagram |  |  | Package Diagram | 
Modified from UML 2
New diagram type
Same as UML 2
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 20: Package Diagram
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Package diagram is used to organize the model
  Groups model elements into a name space
  Often represented in tool browser
  Supports model configuration management (check-in/out)
Model can be organized in multiple ways
  By System hierarchy (e.g., enterprise, system, component)
  By diagram kine (e.g., requirements, use cases, behavior)
  Use viewpoints to augment model organization
Import relationship reduces need for fully qualified name (package1::class1)

## Slide 21: Package Diagram Organizing the Model
By Diagram Type
By Hierarchy
By IPT
pkg SampleModel [by diagram type]
Behavior
Structure
Requirements
Use Cases
pkg SampleModel [by level]
Enterprise
System
Logical Design
Physical Design
EngrAnalysis
Verification
pkg SampleModel [by IPT]
Architecture Team
Requirements Team
IPT A
IPT B
IPT C
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 22: Package Diagram - Views
Viewpoint represents the stakeholder perspective
View conforms to a particular viewpoint
  Imports model elements from multiple packages
  Can represent a model query based on query criteria
View and Viewpoint consistent with IEEE 1471 definitions
pkg SampleModel[by level]
Enterprise
System
Logical Design
Physical Design
Verification
«view» EngrAnalysis
«viewpoint» stakeholders=”…” purpose=”…” constructionRules= ”…” concerns=”…” languages=”…”
EngrAnalysisViewpoint
«import»
«import»
«import»
«import»
«conforms»
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 23: Blocks are Basic Structural Elements
Provides a unifying concept to describe the structure of an element or system
System
Hardware
Software
Data
Procedure
Facility
Person
Multiple standard compartments can describe the block characteristics
  Properties (parts, references, values, ports)
  Operations
  Constraints
  Allocations from/to other model elements (e.g. activities)
  Requirements the block satisfies
  User defined compartments
Compartment Label
values
DutyCycle: Percentage
«block» BrakeModulator
allocatedFrom
«activity»Modulate BrakingForce
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 24: Property Types
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Property is a structural feature of a block
  Part property aka. part (typed by a block)
    Usage of a block in the context of the enclosing (composite) block
    Example - right-front:wheel
  Reference property (typed by a block)
    A part that is not owned by the enclosing block (not composition)
    Example – aggregation of components into logical subsystem
  Value property (typed by value type)
    A quantifiable property with units, dimensions, and probability distribution
    Example
      Non-distributed value: tirePressure:psi=30
      Distributed value: «uniform» {min=28,max=32} tirePressure:psi

## Slide 25: Using Blocks
Based on UML Class from UML Composite Structure
– Supports unique features (e.g., flow ports, value properties)
Block definition diagram describes the relationship among blocks (e.g., composition, association, specialization)
Internal block diagram describes the internal structure of a block in terms of its properties and connectors
Behavior can be allocated to blocks
Blocks Used to Specify Hierarchies and Interconnection
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 26: Block Definition vs. Usage
Definition
Block is a definition/type
Captures properties, etc.
Reused in multiple contexts
Usage
Part is the usage of a block in the context of a composing block
Also known as a role
Block Definition Diagram Internal Block Diagram
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 27: Internal Block Diagram (ibd) Blocks, Parts, Ports, Connectors & Flows
Enclosing Block
Connector Item Flow
Port
Internal Block Diagram Specifies Interconnection of Parts
Part
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 28: Reference Property Explained
S1 is a reference part*
Shown in dashed outline box
*Actual name is reference property
s
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 29: SysML Ports
Specifies interaction points on blocks and parts
  Integrates behavior with structure
  portName:TypeName
Kinds of ports
  Standard (UML) Port
    Specifies a set of required or provided operations and/or signals
    Typed by a UML interface
  Flow Port
    Specifies what can flow in or out of block/part
    Typed by a block, value type, or flow specification
    Atomic, non-atomic, and conjugate variations
Standard Port and Flow Port Support Different Interface Concepts
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 30: Port Notation
Standard Port
Flow Port
provided interface (provides the operations)
item flow
required interface (calls the operations)
Flow Port
part2:
part1:
part1:
part2:
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 31: Delegation Through Ports
Delegation can be used to preserve encapsulation of block (black box vs white box)
Interactions at outer ports of Block1 are delegated to ports of child parts
Ports must match (same kind, type, direction, etc.)
Connectors can cross boundary without requiring ports at each level of nested hierarchy
Child2:
Child1:
ibd [block]Block1[delegation]
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 32: Parametrics
Used to express constraints (equations) between value properties
  Provides support for engineering analysis (e.g., performance, reliability)
  Facilitates identification of critical performance properties
Constraint block captures equations
  Expression language can be formal (e.g., MathML, OCL) or informal
  Computational engine is provided by applicable analysis tool and not by SysML
Parametric diagram represents the usage of the constraints in an analysis context
  Binding of constraint parameters to value properties of blocks (e.g., vehicle mass bound to parameter ‘m’ in F= m  a)
Parametrics Enable Integration of Engineering Analysis with Design Models
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 33: Defining Vehicle Dynamics
Defining Reusable Equations for Parametrics
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 34: Vehicle Dynamics Analysis
4/15/2008 Copyright © 2006-2008 by Object Management Group.
34
Using the Equations in a Parametric Diagram to Constrain Value Properties

## Slide 35: Behavioral Diagrams
SysML Diagram
Use Case Diagram
Activity Diagram
Sequence Diagram
State Machine Diagram
Parametric Diagram
Behavior Diagram |  |  | Requirement Diagram |  |  | Structure Diagram | 
Block Definition Diagram |  |  | Internal Block Diagram |  |  | Package Diagram | 
Modified from UML 2
New diagram type
Same as UML 2
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 36: Activities
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Activity specifies transformation of inputs to outputs through a controlled sequence of actions
Secondary constructs show responsibilities for the activities using activity partitions (i.e., swim lanes)
SysML extensions to Activities
  Support for continuous flow modeling
  Alignment of activities with Enhanced Functional Flow Block Diagram (EFFBD)

## Slide 37: Activity Diagram
Activity Diagram Specifies Controlled Sequence of Actions
Activity
Action
Input
Output
Input
act Example
in1
in2
out1
out2
a2
out1
out1
in1
a5
a1
in1
out1
a3
out1
in1
a4
out1
in1
[x>0]
4/15/2008
Copyright © 2006-2008 by Object Management Group.
[x<=0]
Output

## Slide 38: Routing Flows
Initial Node – On execution of parent control token placed on outgoing control flows
Activity Final Node – Receipt of a control token terminates parent
Flow Final Node – Sink for control tokens
Fork Node – Duplicates input (control or object) tokens from its input flow onto all outgoing flows
Join Node – Waits for an input (control or object) token on all input flows and then places them all on the outgoing flow
Decision Node – Waits for an input (control or object) token on its input flow and places it on one outgoing flow based on guards
Merge Node – Waits for an input (control or object) token on any input flows and then places it on the outgoing flow
Guard expressions can be applied on all flows
38

## Slide 39: Actions Process Flow of Control and Data
Two types of flow
  Object / Data
  Control
Unit of flow is called a “token”
(consumed & produced by actions)
Actions Execution Begins When Tokens Are Available on “all” Control Inputs and Required Inputs
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Control Input
Control Output

## Slide 40: An Action Can Invoke Another Activity
act Activity
Activity is Invoked When an Action Begins to Execute
Control Input
Control Output
action2
action1
4/15/2008
Copyright © 2006-2008 by Object Management Group.
output2
<<optional>>
output1
input2
<<optional>>
input1

## Slide 41: Semantics for Activity Invocation
4/15/2008
Copyright © 2006-2008 by Object Management Group.
A call behavior action can have
0..* control inputs & outputs
0 ..* optional item inputs & outputs
0..* required item inputs & outputs
0..* streaming (and continuous) item inputs & outputs
Starting an action:
An action starts when a token is placed on all of its control inputs and all of its required inputs (must meet minimum multiplicity of its input pins) and the previous invoked activity has completed
An action invokes an activity when it starts, and passes the tokens from its input pins to the input parameter nodes of the invoked activity
During an execution:
An action continues to accept streaming inputs and produce streaming outputs
Terminating an action:
An action terminates when its invoked activity reaches an activity final, or when the action receives a control disable, or as a side affect of other behaviors of the parent activity
The tokens on the output parameter nodes of the activity are placed on the output pins of the action and a control token is placed on each of the control outputs of the action
Following action termination:
The tokens on the output pins and control outputs of the action are moved to the input pins of the next actions when they are ready to start per above
The action can restart and invoke the activity again when the starting conditions are satisfied per above
Note: The summary is an approximation of the semantics.
The detailed semantics are specified in the UML and SysML specification.

## Slide 42: Common Actions
Call Operation Action
(can call leaf level function)
Call Behavior Action
Accept Event Action
(Event Data Pin often elided)
Send Signal Action
(Pins often elided)
act Activity
action2
action1
output2
<<optional>>
output1
input2
<<optional>>
input1
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 43: Activity Diagram Example With Streaming Inputs and Outputs
act Activity
Streaming Inputs and Outputs Continue to Be
output2
output3
<<optional>>
output1
{stream}
input2
<<optional>>
input1
{stream}
action 2
out1
action 1
{stream}
«optional» out1
{stream}
in2
action 4
out1
Start
out1
{stream}
«optional»
in1
{stream}
action 3
Consumed and Produced
While the Action is Executing
4/15/2008
Copyright © 2006-2008 by Object Management Group.
43
«optional»
in1
{stream}
«optional»
in1
[else]
[else]
[x>1]
[y>0]

## Slide 44: Distill Water Activity Diagram (Continuous Flow Modeling)
Continuous Flow Is Representative of Many Physical Processes
Interruptible Region
Actions are enabled by default when activity is enabled
4/15/2008
Copyright © 2006-2008 by Object Management Group.
44
Accept Event Action Will Terminate Execution
Continuous flow means ΔTime
between tokens approaches zero Continuous Flow

## Slide 45: Example – Operate Car
act Operate Car
Turn Key to Off
:Driving
Brake Pressure
«continuous»
«continuous» Brake Pressure
:Braking
«continuous» Modulation Frequency
:Monitor Traction
«continuous» Braking Pressure
«controlOperator»
:Enable on Brake Pressure > 0
{control}
Modulation Frequency
«continuous»
«optional »
Turn Key to On
Enabling and Disabling Actions With Control Operators

## Slide 46: Activity Diagrams Pin vs. Object Node Notation
a1 : Detect Loss of Traction
a2 : Modulate Braking Force
p2 : TractLoss
p1 : TractLoss
of1
act [Activity] Prevent Lockup [ Actions ] act [Activity] Prevent Lockup [ Actions ]
a1 : Detect Loss of Traction
a2 : Modulate Braking Force
tl : TractLoss
Pins are kinds of Object Nodes
  Used to specify inputs and outputs of actions
  Typed by a block or value type
  Object flows connect object nodes
Object flows between pins have two diagrammatic forms
  Pins shown with object flow between them
  Pins elided and object node shown with flow arrows in and out
Pins
ObjectNode
Pins must have same characteristics (name, type etc.)

## Slide 47: Explicit Allocation of Behavior to Structure Using Swimlanes
Activity Diagram (without Swimlanes)
Activity Diagram (with Swimlanes)
act [Activity] Prevent Lockup [ Swimlanes ]
allocatedTo
<<connector>> c2 :
<<allocate>> d1 : Traction Detector
<<allocate>>
m1 : Brake Modulator
a1 : Detect Loss of Traction
a2 : Modulate Braking Force
p2 : TractLoss
p1 : TractLoss
of1
act [Activity] Prevent Lockup [ Actions ]
a1 : Detect Loss of Traction
a2 : Modulate Braking Force
p2 : TractLoss
p1 : TractLoss
of1

## Slide 48: Activity Decomposition
Definition
Use
Prevent Lockup
act [Activity]
[ Actions ]
a1 : Detect Loss of
Traction
a2 : Modulate Braking Force
p2 : TractLoss
p1 : TractLoss
of1
bdd | [Pa ckage] Beh avior [ Beh avior De comp ] |  |  |  | 
a1 <<activity>> De tect Los s of Tra ction |  | <<activity>> Prevent Loc kup p1 <<block>> Tra ctLoss | p2 | a2 <<activity>> Modulate Braki ng Force | 

## Slide 49: SysML EFFBD Profile
Aligning SysML with Classical Systems Engineering Techniques
EFFBD - Enhanced Functional Flow Block Diagram
External Input
External Output
2.1 Serial Function
2.2 Multi- exit Function
2.3 Function in Concurrency
Item 1
2.5 Function in an Iterate
[ before third time ]
Item 2
«optional»
[ after third
time ]
2.6 Output Function
«optional»
Item 3
Item 4
«optional»
«optional»
2.4 Function in Multi-exit Construct
{cc#1}
{cc#2}
«effbd»
act

## Slide 50: Interactions
Sequence diagrams provide representations of message based behavior
  represent flow of control
  describe interactions between parts
Sequence diagrams provide mechanisms for representing complex scenarios
  reference sequences
  control logic
  lifeline decomposition
SysML does not include timing, interaction overview, and communications diagram

## Slide 51: Black Box Interaction (Drive)
4/15/2008 Copyright © 2006-2008 by Object Management Group.
51
sd DriveBlackBox
par
alt controlSpeed
driver:Driver
vehicle: H:ybridSUV
[state = (idle)]
[state = (accelerating/cruising)]
[state = (braking)]
ref
StartVehicleBlackBox
ref
Idle
ref
Accelerate/Cruise
ref
Brake
ref
Steer
ref
Park/ShutdownVehicle
UML 2 Sequence Diagram Scales
by Supporting Control Logic and Reference Sequences

## Slide 52: Black Box Sequence (StartVehicle)
Simple Black Box Interaction
References Lifeline Decomposition For White Box
Interaction
sd StartVehicleBlackBox
driver:Driver
vehicle:HybridSUV
ref StartVehicleWhiteBox
1: StartVehicle
4/15/2008
Copyright © 2006-2008 by Object Management Group.
52
turnIgnitionToStart

## Slide 53: White Box Sequence (StartVehicle)
Decomposition of Black Box Into White Box Interaction
sd StartVehicleWhiteBox
ecu:PowerControlUnit
epc:ElectricalPowerController
1.1: Enable
4/15/2008
Copyright © 2006-2008 by Object Management Group.
52
1: StartVehicle
1.2:ready

## Slide 54: Primary Interaction Operators
Provided by Michael Chonoles
54
ref name
  reference to a sequence diagram fragment defined elsewhere
opt [condition]
  has 1 part that may be executed based on a condition/state value
alt
  has 2 or more parts, but only one executes based on a condition/state
  an operand fragment labeled [else] is executed if no other condition is true
par
  has 2 or more parts that execute concurrently
    Concurrence indicates does not require simultaneous, just that the order is undetermined. If there is only one processor the behavior could be (A then B), (B then A), or (A and B interleaving) …
loop min..max [escape]
  Has a minimum # of executions, and optional maximum # of executions, and optional escape condition
break [condition]
  Has an optional guard. If true, the contents (if any) are executed, and the remainder of the enclosing operator is not executed

## Slide 55: Other Interaction Operators
Provided by Michael Chonoles
54
critical
  The sequence diagram fragment is a critical region. It is treated as atomic – no interleaving with parallel regions
neg
  The sequence diagram fragment is forbidden. Either it is impossible to occur, or it is the intent of the requirements to prevent it from occurring
assert
  The sequence diagram fragment is the only one possible (or legal)
seq (weak, the default)
strict
  Strict: The message exchange occurs in the order described
  Weak: Each lifeline may see different orders for the exchange (subject to causality)
consider (list of messages)
ignore (list of messages)
  Consider: List the messages that are relevant in this sequence fragment
  Ignored: List the messages that may arrive, but are not interesting here

## Slide 56: Trial Result of Vehicle Dynamics
Typical Example of a Timing Diagram
Lifeline are value properties
Timing Diagram Not Part of SysML
timMaxAcceleration [100 Wheel Horsepower]
0.5
0.45
0.4
0.35
0.3
0.25
0.2
0.15
0.1
0.05
0
0 5
15
20
10
Time (sec)
Accelleration (g)
140
120
100
80
60
40
20
0
0
5
10
15
20
Time (sec)
Velocity (mph)
1800
1600
1400
1200
1000
800
600
400
200
0
0
5
15
20
10
Time (sec)
Distance (ft)
Satisfies
«requirementA» cceleration
«diagramDescriptio»n version=”0.1" description=”Constant
100 wheel horsepower, 4000 lb vehicle weight, simple drag" reference=”Equations of Motion” completeness=”assumes perfect tire traction”
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 57: State Machines
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Typically used to represent the life cycle of a block
Support event-based behavior (generally asynchronous)
  Transition with trigger, guard, action
  State with entry, exit, and do-activity
  Can include nested sequential or concurrent states
  Can send/receive signals to communicate between blocks during state transitions, etc.
Event types
  Change event
  Time event
  Signal event

## Slide 58: Operational States (Drive)
stm HSUVOperationalStates
Operate
Idle
Accelerating/ Cruising
Braking
engageBrake/
accelerate/
when (speed = 0)
releaseBrake/
shutOff/stop engine
Off
start[in neutral]/start engine
Nominal states only
keyOff/
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Transition notation: trigger[guard]/action

## Slide 59: Use Cases
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Provide means for describing basic functionality in terms of usages/goals of the system by actors
  Use is methodology dependent
  Often accompanied by use case descriptions
Common functionality can be factored out via
«include» and «extend» relationships
Elaborated via other behavioral representations to describe detailed scenarios
No change to UML

## Slide 60: Operational Use Cases
uc HSUV_UseCases [Operational Use Cases]
HybridSUV
Driver
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Accelerate
Drive_The_Vehi cle
Steer
Brake
«include»
«include»
«include»
Park
«include»
«extend»
Flat_Tire

## Slide 61: Cross-cutting Constructs
Allocations
Requirements
SysML Diagram
Structure Diagram
Behavior Diagram
Use Case Diagram
Activity Diagram
Sequence Diagram
State Machine Diagram
Parametric Diagram
Requirement Diagram
Block Definition Diagram |  |  | Internal Block Diagram |  |  | Package Diagram | 
Modified from UML 2
New diagram type
Same as UML 2
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 62: Allocations
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Represent general relationships that map one model element to another
Different types of allocation are:
  Behavioral (i.e., function to component)
  Structural (i.e., logical to physical)
  Software to Hardware
– ….
Explicit allocation of activities to structure via swim lanes (i.e., activity partitions)
Both graphical and tabular representations are specified

## Slide 63: Different Allocation Representations (Tabular Representation Not Shown)
Explicit Allocation of Action to Part Property
Allocate Relationship
Callout Notation
Compartment Notation
«block» Block Name
part name
allocatedFrom
«elementType» ElementName
Element Name1
Element Name3
Element Name2
«allocate»
«allocate»
Read as follows: “part name has constraints that are allocated to/from an <<element type>> Element Name”
«allocate»
part name : Element Name
action name : Activity Name
«block» Block Name
part name
allocatedFrom
«elementType»Element Name
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 64: SysML Allocation of SW to HW
In UML, the deployment diagram is used to deploy artifacts to nodes
In SysML, «allocation» on an ibd and bdd is used to deploy software/data to hardware
ibd [node] SF Residence
«hardware »
: Site Processor
allocatedFrom
«software» Device Mgr
«software» Event Mgr
«software» Site Config Mgr
«software» Site RDBMS
«software» Site Status Mgr
«software» User I/F
«software» User Valid Mgr
*
«hardware »
: Optical Sensor
«hardware »
: DSL Modem
2
«hardware »
: DVD-ROM Drive
allocatedFrom
«data» Video File
«hardware »
: User Console
2
«hardware »
: Video Camera
«hardware »
: Alarm
«hardware »
: NW Hub
allocatedFrom
«software» SF Comm I/F
«hardware »
: Site Hard Disk
allocatedFrom
«data» Site Database
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 65: Requirements
4/15/2008
Copyright © 2006-2008 by Object Management Group.
The «requirement» stereotype represents a text based requirement
  Includes id and text properties
  Can add user defined properties such as verification method
  Can add user defined requirements categories (e.g., functional, interface, performance)
Requirements hierarchy describes requirements contained in a specification
Requirements relationships include DeriveReqt, Satisfy, Verify, Refine, Trace, Copy

## Slide 66: Requirements Breakdown
Requirement Relationships Model the Content of a Specification
req [package] HSUVRequirements [HSUV Specification]
«requirement» Eco-Friendliness
«requirement» Performance
«requirement» Braking
«requirement» FuelEconomy
«requirement» Acceleration
«requirement» Emissions
Id = “R1.2.1”
text = “The vehicle shall meet Ultra-Low Emissions Vehicle standards.”
HSUVSpecification
RefinedBy
«useCase» HSUVUseCases::Accelerate
SatisfiedBy
«block» PowerSubsystem
VerifiedBy
«testCase» MaxAcceleration
«requirement» Power
«deriveReqt»
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 67: Example of Derive/Satisfy Requirement Dependencies
Client
Supplier
Arrow Direction Opposite Typical Requirements fFrom OlMoG w-Down
Client depends on supplier (i.e., a change in supplier results in a change in client)
«requirement» Acceleration
«requirement» CargoCapacity
«requirement» OffRoadCapability
Supplier
«deriveReqt»
«block» PowerSubsystem
«satisfy»
Client
«requirement» Power
«deriveReqt»
4/15/2008
Copyright © 2006-2008 by Object Management Group.
«deriveReqt»
from OMG

## Slide 68: Problem and Rationale
Problem and Rationale can be attached to any Model Element to Capture Issues and Decisions
bdd Master Cylinder requirements
«requirement»
Loss of Fluid
«requirement»
Reservoir
«block»
Brake System
m:MasterCylinder
«satisfy»
«satisfy»
«rationale»
The best-practice solution consists in assigning one reservoir per brakeline. See "automotive_d32_hdb.doc"
«problem»
The master cylinder in previous version leaked.
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 69: Stereotypes & Model Libraries
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Mechanisms for further customizing SysML
Profiles represent extensions to the language
  Stereotypes extend meta-classes with properties and constraints
    Stereotype properties capture metadata about the model element
  Profile is applied to user model
  Profile can also restrict the subset of the meta-model used when the profile is applied
Model Libraries represent reusable libraries of model elements

## Slide 70: Stereotypes
Defining the Stereotype
Applying the Stereotype
«metaclass»
NamedElement
«stereotype»
ConfigurationItem
author: String version: String lastChanged: Date
«configurationItem»
Engine
author=”John Doe” version=”1.2" lastChanged=Dec12, 2005
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 71: Applying a Profile and Importing a Model Library
pkg ModelingDomain [Establishing HSUV Model]
«modelLibrary»
SI Definitions
«import»
«profile»
SysML
HSUVModel
«apply»
{strict}
«apply» {strict}
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 72: Cross Connecting Model Elements
4/15/2008 Copyright © 2006-2008 by Object Management Group.
72
1. Structure 2. Behavior
3. Requirements
4. Parametrics
satisfy

## Slide 73: SysML Modeling as Part of the SE Process

## Slide 74: Distiller Sample Problem
Refer to Chapter 15
“A Practical Guide to SysML”

## Slide 75: Distiller Problem Statement
The following problem was posed to the SysMLteam in Dec ’05 by D. Oliver:
Describe a system for purifying dirty water.
  Heat dirty water and condense steam are performed by a Counter Flow Heat Exchanger
  Boil dirty water is performed by a Boiler
  Drain residue is performed by a Drain
  The water has properties: vol = 1 liter, density 1 gm/cm3, temp 20 deg C, specific heat 1cal/gm deg C, heat of vaporization 540 cal/gm.
A crude behavior diagram is shown.
What are the real requirements? How do we design the system?
75

## Slide 76: Distiller Types
Batch Distiller
Continuous Distiller
Note: Not all aspects of the distiller are modeled in the example
75

## Slide 77: Distiller Problem – Process Used
75
Organize the model, identify libraries needed
List requirements and assumptions
Model behavior
  In similar form to problem statement
  Elaborate as necessary
Model structure
  Capture implied inputs and outputs
    segregate I/O from behavioral flows
  Allocate behavior onto structure, flow onto I/O
Capture and evaluate parametric constraints
  Heat balance equation
Modify design as required to meet constraints
Model the user interaction
Modify design to reflect user interaction

## Slide 78: Distiller Problem – Package Diagram: Model Structure and Libraries
75

## Slide 79: Distiller Example Requirements Diagram
75

## Slide 80: Distiller Example: Requirements Tables
table [requirement] OriginalStatement[Decomposition of OriginalStatement]
id | name | text
S0.0 | OriginalStatement | Describe a system for purifying dirty water. …
S1.0 | PurifyWater | The system shall purify dirty water.
S2.0 | HeatExchanger | Heat dirty water and condense steam are performed by a …
S3.0 | Boiler | Boil dirty water is performed by a Boiler.
S4.0 | Drain | Drain residue is performed by a Drain.
S5.0 | WaterProperties | water has properties: density 1 gm/cm3, temp 20 deg C, …
S5.1 | WaterInitialTemp | water has an initial temp 20 deg C
table [requirement] PurifyWater[Requirements Tree]
75
id | name | relation | id | name | Rationale
S1.0 | PurifyWater | deriveReqt | D1.0 | DistillWater | The requirement for a boiling function and a boiler implies that the water must be purified by distillation

## Slide 81: Distiller Example – Activity Diagram: Initial Diagram for DistillWater
Energy to Pure
Dirty water Dirty water condense water @ 20 deg C @ 100 deg C Steam
Condense steam
Heat Dirty water Boil Dirty water and andand
To 100 deg C
Drain Residue
Residue
Heat to Dirty Disposed
water Heat to Boil residue
water
This activity diagram applies the SysML EFFBD profile, and formalizes the diagram in the problem statement.
Actions (Functions)
Control (Sequence) Things that flow (ObjectNodes)
75

## Slide 82: Distiller Example – Activity Diagram: Control-Driven: Serial Behavior
Batch Distiller
Continuous Distiller Here
«effbd»
act [activity] DistillWater [Simple Starting Point)
coldDirty:H2O
[liquid]
hotDirty:H2O [liquid]
steam:H2O [gas]
pure:H2O
[liquid]
predischarge :Residue
discharge :Residue
external:Heat
recovered:Heat
a3:CondenseSteam
a1:HeatWater
a2:BoilWater
a4:DrainResidue
75

## Slide 83: Distiller Example – Block Definition Diagram: DistillerBehavior
Control (not shown on BDD)
Need to consider phases of H20
Activities (Functions)
Things that flow (ObjectNodes)
75

## Slide 84: Distiller Example – State Machine Diagram: States of H2O
Transitions
States
75

## Slide 85: Distiller Example – Activity Diagram: I/O Driven: Continuous Parallel Behavior
Continuous Distiller
75
Batch Distiller Here

## Slide 86: Distiller Example – Activity Diagram: No Control Flow, ActionPin Notation, Simultaneous Behavior
75

## Slide 87: Distiller Example – Activity Diagram (with Swimlanes): DistillWater
Parts
4/15/2008 Allocated ibd Copyright © 2006-2008 by Object Management Group.
87

## Slide 88: Distiller Example – Block Definition Diagram: DistillerStructure
88

## Slide 89: Distiller Example – Block Definition Diagram: Heat Exchanger Flow Ports
pkg
c in : Fluid
c out : Fluid
h in : Fluid
<<block>>
Boiler
h out : Fluid bottom : Fluid
bottom : Heat
middle : Fluid
top : Fluid
<<block>>
Distiller
<<block>>
Valve
in : Fluid
out : Fluid
drain
or
condenser | evaporat | 
<<block>> |  | 
Heat Exchanger |  | 
constraints |  | 
{h out.temp<=120, c in.temp<=60, h in.temp<=120, c out.temp<=90} |  | 
Flow Ports
(typed by things that flow)
Constraints (on Ports)
bdd Initial Distiller Structure [ distiller breakdown (ports) ]
88

## Slide 90: Distiller Example – Internal Block Diagram: Distiller Initial Design
ibd
88

## Slide 91: Distiller Example –Table: Functional Allocation
Exercise for student:
Is allocation complete? Where is “«objectFlow»of8”?
Swimlane Diagram
88

## Slide 92: Parametric Diagram: Heat Balance
88

## Slide 93: Distiller Example – Heat Balance Results
table IsobaricHeatBalance1 [Results of Isobaric Heat Balance]
specific heat cal/gm-°C
1
latent heat cal/cm
540
main3 : H2O
main4 : H2O
mass flow rate gm/sec
6.8
6.8
1 1 1
temp °C
20
100
100 100 100
dQ/dt cooling water cal/sec | 540
dQ/dt steam-condensate cal/sec | 540
condenser efficency | 1
heat deficit | 0
dQ/dt condensate-steam cal/sec | 540
boiler efficiency | 1
dQ/dt in boiler cal/sec | 540
main1 : H2O
main2 : H2O frm condenser
main2 : H2O into evap
Note: Cooling water needs to have 6.75x
flow of steam!
Need bypass between hx_water_out and bx_water_in!
Satisfies «requirement» WaterSpecificHeat
Satisfies «requirement» WaterHeatOfVaporization
Satisfies «requirement»
WaterInitialTemp
Set these (steady state)
Solve for these
88

## Slide 94: Distiller Example – Activity Diagram: Updated DistillWater
88

## Slide 95: Distiller Example – Internal Block Diagram: Updated Distiller
4/15/2008 Copyright © 2006-2008 by Object Management Group. 95
ibd

## Slide 96: Distiller Example – Use Case and Sequence Diagrams
sd [Interaction] Operational Sequence [ simple seqence ]
per
ini
: Operator
<<block>>
: Distiller
1: Turn On
2: Power Lamp On
4: High Level Lamp On
5: Low Level Lamp On
6: Draining Lamp On
3: Operating Lamp On
7: Turn Off
8: Power Lamp Off
[while state=Ope
rating]
[state=drain
ing residue]
[level=low]
alt
[level=high]
loop
uc [Package] Distiller Use Cases [ use case example ]
Distiller
Operate Distiller
Operator
96

## Slide 97: Distiller Example – Internal Block Diagram: Distiller Controller
class
pwr in : Elec Power
pwr : Elec Power
v1 : V Ctrl
v2 : V Ctrl
b : Boiler Signals bp : Elec Power
heat & valve : Controller
condenser : Heat Exchanger
evaporator : Boiler
p in : Elec Power
c : Boiler Signals
drain : Valve
v : V Ctrl
user : Control Panel
splitter : Tee Fitting
main4 : H2O
m2.2 : H2O
distiller pwr : Elec Power
feed ctl : V Ctrl
htr pwr : Elec Power
drain ctl : V Ctrl
blr status : Blr Sig
blr ctl : Blr Sig
main2 : H2O
sludge1 : Residue
main3 : H2O
sludge2 : Residue
main1 : H2O
v : V Ctrl
m2.1 : H2O
m2.1 : H2O
feed : Valve
iPanel
iPanel
ibd Distiller [ block diagram revised & elaborated]
diverter assembly
96

## Slide 98: Distiller Example – State Machine Diagram: Distiller Controller
stm Controller State Machine [ simple diagram]
Operating
do /bx heater on
Level High
do /open drain : Valve
Level Low
do /open feed : Valve
Level OK
do /shut all Valves
Cooling Off
entry /bx1 heater OFF
do /open feed : Valve, open drain : Valve
Filling
do /open feed : Valve
Draining
do /open drain : Valve
Warming Up
do /bx1 heater on
[bx1 level high]
[NOT bx1 level high]
[bx1 level low]
[NOT bx1 level low]
Building Up Residue [residue timer] Purging Residue
do /close drain : Valve [drain timer] do /open drain : Valve
[bx level low]
[power = on]
[shutdown command]
[bx1 temp = 100]
[NOT bx1 level low]
[bx1 temp = 30]
Off
do /Power Light Off
96

## Slide 99: OOSEM – ESS Example
Refer to Chapter 16
“A Practical Guide to SysML”

## Slide 100: System Development Process
System Modeling Activities
Integrated Product Development (IPD) is essential to improve communications
A Recursive V process that can be applied to multiple levels of the system hierarchy
Component Modeling Activities
Manage System Development
Define System Reqt's & Design
Integrate & Test System
System
Stakeholder Reqts
System arch Allocated reqt's
Procedures
Data Hardware Software Develop
System Components
Verified System Component
Plan
Copyright © 2006-2008 by Object Management Group.
100
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006
Status Technical data
Test procedures

## Slide 101: System Modeling Activities – OOSEM Integrating MBSE into the SE Process
Synthesize Allocated Architecture
Define System Requirements
Define Logical Architecture
Optimize & Evaluate Alternatives
Support Validation & Verification
Analyze Needs
Major SE Development Activities
Common Subactivities
Parametric Diag
Trade study
Test cases
Test procedures
Causal analysis
Mission use cases/scenarios
Enterprise model
System use cases/scenarios
Elaborated context
Logical decomposition
Logical scenarios
Logical subsystems
Node diagram
HW, SW, Data arch
System deployment
Manage Requirements
Reqt’s Diagram & tables
Copyright © 2006-2008 by Object Management Group.
101
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 102: Enhanced Security System Example
The Enhanced Security System is the example for the OOSEM material
  Problem fragments used to demonstrate principles
  Utilizes Artisan RTS™ Tool (early version) for the SysML artifacts
Copyright © 2006-2008 by Object Management Group.
2006102
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006102

## Slide 103: ESS Requirements Flowdown
ESS System Models
ESS Enterprise Models
ESS Logical Design Models
ESS Allocated Design Models
«document»
Market Needs
id# = SS1
«requirement»
ESS System Specification
id# = LR1
«requirement»
ESS Logical Requirements
id# = AR1
«requirement»
ESS Allocated Requirements
id# = SS102
txt = System shall detect intruder entry and exit ...
«requirement»
IntruderDetection
«requirement»
R111
«trace»
«deriveReqt» id# = SS111
«deriveReqt»
«refine»
«refine»
«refine»
«trace»
«satisfy»
«satisfy»
«satisfy»
satisfiedBy
Entry/Exit Subsystem
verifiedBy
Entry/Exit Detection Test
req [package] ESS Requirements Flowdown
Copyright © 2006-2008 by Object Management Group.
2006103
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006103

## Slide 104: Operational View Depiction
Central Monitoring Station As-Is
Police
Residence
Dispatcher
Intruder
Comm Network
bdd [package] Enterprise (As Is)
Copyright © 2006-2008 by Object Management Group.
2006104
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006104

## Slide 105: ESS Enterprise As-Is Model
Copyright © 2006-2008 by Object Management Group.
2006105
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006105

## Slide 106: ESS Operational Enterprise To-Be Model
Copyright © 2006-2008 by Object Management Group.
2006106
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006106

## Slide 107: System Use Cases - Operate
Operate
Monitor Site
Respond
Respond to Break-In
Respond to Fire
Respond to Medical
«include»
«include»
«extend»
uc [package] System Use Cases
Activate/Dea- ctivate
Copyright © 2006-2008 by Object Management Group.
2006107
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006107

## Slide 108: System Scenario: Activity Diagram Monitor Site (Break-In)
act Monitor Site (break in)
Enter Property
Conduct Theft
Exit Property
«actor» Intruder
Status Update
DetectEntry
GenerateAlarm
ReportEntry
ReportExit
«system» ESS
Assess Report
Report Update
Dispatch Police
«external» Emergency Services
ValidateEntry
Validated Entry
InternalMonitor
[Alert]
DetectExit
[Alert]
[Alert]
System On
System Off
Copyright © 2006-2008 by Object Management Group.
2006108
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006108

## Slide 109: ESS Elaborated Context Diagram
Copyright © 2006-2008 by Object Management Group.
2006109
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006109

## Slide 110: ESS Logical Decomposition (Partial)
110

## Slide 111: Detect Entry Scenario
act detectEntry
Sense State Change
wi : Window Input
di : Door Input
ee : SensedEntry
«logical»
Entry Sensor
«logical» Entry/Exit Monitor
Alert Status
log : Event
status
Record Event
estatus
«store» Event Log
«logical» Event Monitor
«subsystem» entry/exit subsystem
«continuous» Door Input
«continuous» Window Input
Detect Event
sensor : SensorOutput status[State=BreakInResponse]
[Else]
110

## Slide 112: Elaborating Logical Component
Added operations from Detect Entry / Detect Exit logical scenario
These operations support entry/exit subsystem
Sense State Change()
Detect event()
«logical»
Entry/Exit Monitor
«logical»
Entry Sensor
«logical»
Event Monitor
Record event()
«store»: Event Log
110

## Slide 113: ESS Logical Design – Example Subsystem
Copyright © 2006-2008 by Object Management Group.
113
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 114: ESS Logical Design (Partial)
«logical»
: Entry Sensor
«logical»
: Exit Sensor
«logical»
: Emergency Monitor
«logical»
: Emer Serv I/F
«logical»
: Event Monitor
«store»
: Event Log
«logical»
: Alarm I/F
«logical»
: Alarm Generator
«logical»
: Perimeter Sensor
«logical»
: Environment Sensor
«logical»
: Fault Mgr
«logical»
: Customer Output Mgr
«logical»
: Customer I/F
«logical»
: Entry/Exit Monitor
: Door Input
: Window Input
: Door Input
: Window Input
: EmergencyData
: Emergency ServicesOut
: Alert Status
: AlarmCmd
: AlarmSignal
: Alert Status
: BIT
: FaultReport
: Fault
: BIT
: BIT
: BIT
: Lamp
: Entry/Exit Alert Status
: SensedExit
: SensedEntry
ibd [system] ESS
Copyright © 2006-2008 by Object Management Group.
113
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 115: ESS Allocation Table (partial)
 |  |  | Logical Components |  |  |  |  |  |  |  |  |  |  |  | 
Physical Components | Type |  | Entry Sensor | Exit Sensor | Perimeter Sensor | Entry/Exit Monitor | Event Monitor | Site Comms I/F | Event Log | Customer I/F | Customer Output Mgr | System Status | Fault Mgr | Alarm Generator | Alarm I/F
 | «software» | Device Mgr |  |  |  |  |  |  |  |  |  |  |  |  | X
 |  | SF Comm I/F |  |  |  |  |  | X |  |  |  |  |  |  | 
 |  | User I/F |  |  |  |  |  |  |  |  | X |  |  |  | 
 |  | Event Mgr |  |  |  | X | X |  |  |  |  |  |  |  | 
 |  | Site Status Mgr |  |  |  |  |  |  |  |  |  |  | X |  | 
 |  | Site RDBMS |  |  |  |  |  |  | X |  |  | X |  |  | 
 |  | CMS RDBMS |  |  |  |  |  |  | X |  |  |  |  |  | 
 | «data» | Video File |  |  |  |  |  |  | X |  |  |  |  |  | 
 |  | CMS Database |  |  |  |  |  |  | X |  |  |  |  |  | 
 |  | Site Database |  |  |  |  |  |  | X |  |  | X |  |  | 
 | «hardware» | Optical Sensor | X | X |  |  |  |  |  |  |  |  |  |  | 
 |  | DSL Modem |  |  |  |  |  | X |  |  |  |  |  |  | 
 |  | User Console |  |  |  |  |  |  |  | X |  |  |  |  | 
 |  | Video Camera |  |  | X |  |  |  |  |  |  |  |  |  | 
 |  | Alarm |  |  |  |  |  |  |  |  |  |  |  | X | 
Allocating Logical Components to HW, SW, Data, and Procedures components
Copyright © 2006-2008 by Object Management Group.
113
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 116: ESS Deployment View
Copyright © 2006-2008 by Object Management Group.
113
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 117: ESS Parametric Diagram To Support Trade-off Analysis
Copyright © 2006-2008 by Object Management Group.
113
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 118: Entry/Exit Test Case
Description
Door[1]
/:Optical Sensor
«sut»
«hardware»
«sut»
«hardware»
:Site Processor
«sut»
«hardware»
:DSL Modem
«sut»
«hardware»
Window[4]
/:Optical Sensor
«testComponent»
:IntruderEmulator
seq
seq
Intruder enters through front
Enter
door
Door sensor detects entry
: SensedEntry
New alert status sent to central
system
IntruderEntry : Alert Status
Intruder leaves through lounge
window
Exit
Window sensor detects exit
: SensedExit
Changed alert status sent to
central system
Intruder Exit : Alert Status
sd Entry/Exit Detection Test
Copyright © 2006-2008 by Object Management Group.
113
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 119: OOSEM Browser View Artisan Studio™ Example
Copyright © 2006-2008 by Object Management Group.
4/15/2008 119
Copyright © Lockheed Martin Corporation 2000 – 2003 & INCOSE 2004-2006

## Slide 120: SysML in a Standards Framework

## Slide 121: Systems Engineering Standards Framework (Partial List)
Process Standards
Modeling & Simulation Standards
Modeling Methods
Architecture Frameworks
Interchange & Metamodeling Standards
STEP/AP233
XMI
FEAF DoDAF MODAF Zachman FW
IDEF0 MARTE HLA MathML
System Modeling Simulation & Analysis
EIA 632 ISO 15288 IEEE 1220 CMMI
HP OOSE SADT Other
MOF
SysML
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 122: ISO/IEC 15288 System Life Cycle Processes
Enterprise Processes
5.3.2
Enterprise Environment Management Process
5.3.3
Investment Management Process
5.3.6
Resource Management Process
5.3.5
Quality Management Process
5.3.4
System Life Cycle Processes Management
5.2.3
Supply Process
5.2.2
Acquisition Process
Agreement Processes
Project Processes
5.4.2
Project Planning Process
5.4.3
Project Assessment Process
5.4.6
Risk Management Process
5.4.5
Decision-Making Process
5.4.4
Project Control Process
5.4.8
Information Management Process
5.4.7
Configuration Management Process
Technical Processes
5.5.2
Stakeholder Reqts Definition Process
5.5.3
Reqts Analysis Process
5.5.6
Integration Process
5.5.5
Implementation Process
5.5.8
Transition Process
5.5.7
Verification Process
5.5.9
Validation Process
5.5.10
Operation Process
5.5.11
Maintenance Process
5.5.12
Disposal Process
5.5.4
Architectural Design Process
4/15/2008
Copyright © 2006-2008 by Object Management Group.

## Slide 123: Standards-based Tool Integration with SysML
•
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
.....
.....
.....
AP233/XMI
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Model/Data Interchange
AP233/XMI
Systems Modeling Tool
Other Engineering Tools

## Slide 124: Participating SysML Tool Vendors
4/15/2008
Copyright © 2006-2008 by Object Management Group.
Artisan (Studio)
EmbeddedPlus (SysML Toolkit)
– 3rd party IBM vendor
No Magic (Magic Draw)
Sparx Systems (Enterprise Architect)
IBM (Tau and Rhapsody)
TopCased
Visio SysML template

## Slide 125: Transitioning to SysML

## Slide 126: Using Process Improvement To Transition to SysML
126

## Slide 127: MBSE Transition Plan
126
MBSE Scope
MBSE Responsibilities/Staffing
Process guidance
  High level process flow (capture in SEMP)
  Model artifact checklist
  Tool specific guidance
Tool support
  Modeling tool
  Requirements management
  CM
Training
Schedule

## Slide 128: Typical Integrated Tool Environment
Project Management
CM/DM
Product Data Management
Requirements Management
Verification & Validation
Simulation & Visualization
SoS/ DoDAF / Business Process Modeling
System Modeling SysML
Software Modeling UML 2.0
Hardware Modeling VHDL, CAD, ..
Engineering Analysis
126

## Slide 129: Summary and Wrap up

## Slide 130: Summary
130
SysML sponsored by INCOSE/OMG with broad industry and vendor participation and adopted in 2006
SysML provides a general purpose modeling language to support specification, analysis, design and verification of complex systems
  Subset of UML 2 with extensions
  4 Pillars of SysML include modeling of requirements, behavior, structure, and parametrics
Multiple vendor implementations available
Standards based modeling approach for SE expected to improve communications, tool interoperability, and design quality
Plan SysML transition as part of overall MBSE approach
Continue to evolve SysML based on user/vendor/researcher feedback and lessons learned

## Slide 131: References
130
OMG SysML website
  http://www.omgsysml.org
  Refer to current version of SysML specification, vendor links, tutorial, and papers
A Practical Guide to SysML (Morgan Kaufmann) by Friedenthal, Moore, Steiner
  http://www.elsevierconnect.com/companion.jsp?ISBN=9780123743794
UML for Systems Engineering RFP
– OMG doc# ad/03-03-41
UML 2 Superstructure v2.1.2
  OMG doc# formal/2007-11-02
UML 2 Infrastructure v2.1.2
  OMG doc# formal/2007-11-04
OMG SysML Information Days Presentations (Dec 8-11, 2008)
  http://www.omg.org/news/meetings/tc/santa_clara/special-events/SysML_Agenda.htm
PAPERS
Integrating Models and Simulations of Continous Dynamics into SysML
  Thomas Johnson, Christiaan Paredis, Roger Burkhart, Jan ‘2008
Simulation-Based Design Using SysML - Part 1: A Parametrics Primer
  RS Peak, RM Burkhart, SA Friedenthal, MW Wilson, M Bajaj, I Kim
Simulation-Based Design Using SysML - Part 2: Celebrating Diversity by Example
  RS Peak, RM Burkhart, SA Friedenthal, MW Wilson, M Bajaj, I Kim
SysML and UML 2.0 Support for Activity Modeling,
  Bock. C., vol. 9 no.2, pp. 160-186, Journal of International Council of Systems Engineering, 2006.
The Systems Modeling Language,
  Matthew Hause, Alan Moore, June ' 2006.
An Overview of the Systems Modellng Language for Products and Systems Development,
  Laurent Balmelli, Oct ' 2006.
Model-driven systems development,
  L. Balmelli, D. Brown, M. Cantor, M. Mott, July ' 2006.
TUTORIAL AUTHORS
Sanford Friedenthal (sanford.friedenthal@lmco.com)
Alan Moore (alan.moore@mathworks.co.uk)
Rick Steiner (fsteiner@raytheon.com)

## Slide 132: Class Exercise Dishwasher Example Sample Artifacts
130
Primary
Requirement diagram – dishwasher spec
Block definition diagram – top level
Internal block diagram – dishwasher black box
Use case diagram
Activity diagram – black box scenario
Block definition diagram – input/output definitions
Block definition diagram – dishwasher hierarchy
Internal block diagram – dishwasher white box
Activity diagram – white box scenario
Requirement diagram - traceability
Optional
Parametric diagram
State machine diagram
Sequence diagram